## Slide 1: Fieldtrip Crash Course
Nick Del Grosso
Warning: Not completed

## Slide 2: Why use Matlab for Your Analysis?
More Control
Less Experimenter Bias = More Objective Results
Quicker Analysis Time
“Batchable”
Easy to Customize
More Time Thinking = More Time Achieving
Matlab is easy-to-use, general to use
If you are spending your time
doing work that anyone can do,
Then you are not living up to your potential as a researcher!

## Slide 3: Why Use Fieldtrip?
Functions correspond directly to Analysis Steps:
  Ex) Define your trials using ft_definetrial.
  Ex) Preprocess your data using ft_preprocessing
Functions are simple to implement.
  All functions have the same inputs:
    cfg: select settings for the function, like filter settings, trial lengths, etc.
    data: the data you want the function to work on
Computationally Efficient
Automatically detects and imports most major data formats
Free, Open-Source, Customizable, and Constantly updated
  It is often simple to implement the latest analysis techniques and have confidence in your results!

## Slide 4: Overview 1: Steps in an ERP analysis
General
Fieldtrip
Set your Trial length, decide what events to time-lock use.
Import your data, filter, baseline-correction, data transformation.
Reject artifacts based on: visual or threshold
ft_definetrial
ft_preprocessing
ft_artifact_eog, ft_rejectvisual, ft_rejectartifact.

## Slide 5: ft_definetrial
Format: cfg = ft_definetrial(cfg);
Makes cfg.trl, which contains a list of what data samples correspond to trials
clear cfg
cfg.dataset = (filename of your eeg data file)
cfg.trialdef.eventtype = ‘trigger’ (can be ‘?’)
cfg.trialdef.eventvalue = trigger number to use
cfg.trialdef.prestim = time before trigger in trial
cfg.trialdef.poststim = time after trigger in trial

## Slide 6: ft_preprocessing
Format: data = ft_preprocessing(cfg,data)
Imports your data and does all initial filtering and transformations.
(lots of options: see help for full list)
cfg.lpfilter = use lowpass filter (‘yes’ or ‘no’)
cfg.lpfreq = lowpass cutoff freq (in Hz)
cfg.dftfilter = use 50 hz notch filter (‘yes’ or ‘no’)
cfg.dftfreq = [50 100 150] (europe only)
cfg.demean = use baseline correction (‘yes’ or ‘no’)
cfg.baselinewindow = [begin end] time to use for baseline correction

## Slide 7: ft_rejectvisual
Format: data = ft_rejectvisual(cfg,data);
Plots ERPs for each trial and allows you to select bad trials (due to artifact) to reject using a graphical interface
Allows transformation using cfg settings (see help), but if using for blinks and if you recorded EOG no transformation is necessary.
clear cfg
cfg.trials = ‘all’;

## Slide 8: Overview 2: Steps in a basic ERP analysis
General
Fieldtrip
Component Decomposition (ICA, PCA, other methods)
Artifact Component Rejection
Separate Conditions
ft_componentanalysis
ft_rejectcomponent
ft_redefinetrial
ft_timelockanalysis
ft_multiplotER , ft_topoplotER

## Slide 9: ft_componentanalysis
Format: comp = ft_componentanalysis(cfg,data);
Performs ICA, PCA, or other component decomposition. Useful for lots of things, but we’ll just use it here to identify and remove signals that represent certain artifact types
clear cfg
cfg.method = what method to use (default: ‘runica’)
cfg.demean = subtract trial means (‘yes’ or ‘no’)
cfg.runica.extended = whether to use extended algorithm to change based on subnormal component distributions (1, 0, or negative number)

## Slide 10: ft_componentbrowser and ft_rejectcomponent
Format: ft_componentbrowser(cfg,comp)
Visualize components, browse using a graphical interface
clear cfg
cfg.layout = your electrode layout file
Format: ft_rejectcomponent(cfg,comp)
Visualize components, browse using a graphical interface
clear cfg
cfg.layout = your electrode layout file

## Slide 11: Overview 3: Steps in a basic ERP analysis
General
Fieldtrip
Average ERPs of each condition
Plot Averaged ERPs
Run Statistics
ft_timelockanalysis
ft_multiplotER, ft_topoplotER
ft_timelockstatistics